## Slide 1: Vessel Visualization using Curvicircular Feature Aggregation
-Raphael Krauthann

## Slide 2: Agenda
Medical Background
Algorithm
Discussion and Limitations
Alternatives and Comparison
Conclusion

## Slide 3: Medical Background
The average human…
…has 96.000km of blood vessels
…pumps 6L of blood every minute
…has 7% of his bodyweight consisting of blood
https://www.livescience.com/39925-circulatory-system-facts-surprising.html

## Slide 4: Medical Background
What are Cardiovascular diseases?
  Diseases of blood vessels supplying
    Brain (cerebrovascular)
    Heart (coronary)
    Arms and Legs (peripheral)
  Heart Diseases
  Thrombosis (blood clots that can move to heart/brain/lungs)
CVDs number one cause of death globally
(estimated 17,9 million in 2016 / 31%)
https://www.who.int/news-room/fact-sheets/detail/cardiovascular-diseases-(cvds)

## Slide 5: Medical Background
“People with cardiovascular disease or who are at high cardiovascular risk […] need early detection and management using counselling and medicines, as appropriate.”
- WHO

## Slide 6: Medical Background
Fast and precise diagnosis is key
Complex data is time-intensive to analyze
  Many slices are generated
  All viewing angles need to be reviewed
On Computed Tomography Angiography (CTA) data, one angle is not enough to distinguish completely from partially calcificated vesslels

## Slide 7: About Curvicircular Feature Aggregation (CFA)
Reducing the amount of interaction
Removing the need to rotate around the vessel
  Creating a single static image
Based on Maximum Intensity Projection (MIP) and Curved Planar Reformation (CPR)

## Slide 8: Algorithm

## Slide 9: About Curved Planar Reformation (CPR)
Planar cuts along given path (most likely vessels)
Images can be isometric depending on used algorithm
Types: projected, stretched, straightened
Multipath-CPRs possible with multiple branches

## Slide 10: Algorithm - Vessel
Just like in CPR, the centerlines are calculated for the vessel, resulting in centerpoints on which samples can be made
Vessel radius is determined (or should be available) for each slice
For each centerpoint the direction of the vessel needs to be found

## Slide 11: Algorithm - Sampling
For each reformed slice circular rays are cast, either at constant angles or constant arc-length
  (constant arc-length may result in long computations on high radii)

## Slide 12: Algorithm - Sampling
n are the numbers of samples
X is the center
r and s are the projecting vectors of the plain
  (1,0,0) and (0,1,0) if the vessel is orthogonal on the plane
R is the radius of the current circular ray cast

## Slide 13: Algorithm - Sampling

## Slide 14: Algorithm - Aggregation
For every slice the values of all ray casts are aggregated using either
  MIP detects complete califications
  Minimum Intensity Projection (MINIP) detects minor plaque
  Average Intensity Projection (AVG)
MIP and MINIP are medically the most interesting
The two are presented next to each other

## Slide 15: Algorithm - Aggregation

## Slide 16: Algorithm - Aggregation
Other aggregation operators possible like AVG
  Have to be order independent (like min or max)

## Slide 17: Algorithm – Context (optional)
I_CTX is the context image data
Within the vessel the context image data should be used
The factor f should be greater then one to make sure the context image starts outside the vessel (2 in the paper implementation)

## Slide 18: Algorithm – Stability (optional)
i and j are within [–w;w], where w is a user defined positive integer
r and are orthogonal vectors
These points are samples, and the variance between them is the indicator for the stability
High variances are marked red

## Slide 19: Algorithm – Stability (optional)

## Slide 20: Visual Mapping
For every slice the values of all ray casts are aggregated using either
  MIP detects complete califications
  Minimum Intensity Projection (MINIP) detects minor plaque
  Average Intensity Projection (AVG)
MIP and MINIP are medically the most interesting
The two are presented next to each other

## Slide 21: Visual Example

## Slide 22: Discussion and Limitations
Problems:
  Specific rotation or Size can not be determined
    MINIP only shows plaque
    MIP only shows calcifications
  Errors if the centerline cannot be determined accurately
Advantages:
  Gives information about stability of centerlines
  Less sensitive to changes of the centerline

## Slide 23: Comparison and Evaluation

## Slide 24: Comparison and Evaluation

## Slide 25: Comparison and Evaluation

## Slide 26: Comparison and Evaluation
9 radiologists have been asked to evaluate the performance of the given images in 5 categories (a)
Additionally they should give their opinion if a specific information is valuable (b)

## Slide 27: Discussion and Limitations
Problems:
  Specific rotation or Size can not be determined
    MINIP only shows plaque
    MIP only shows calcifications
  Errors if the centerline cannot be determined accurately
Advantages:
  Gives information about stability of centerlines
  Less sensitive to changes of the centerline

## Slide 28: Literature
G. Mistelbauer et al., “Vessel Visualization using Curvicircular Feature Aggregation,” Computer Graphics Forum, vol. 32, no. 3pt2, pp. 231–240, 2013.
Bühler K., Felkel P., Cruz A. L.: Geometric Methods for Vessel Visualization and Quantiﬁcation - A Survey. Springer, 2004, ch. in Geometric Modeling for Scientiﬁc Visualization, pp. 399–419.
Wang W., Jüttler B., Zheng D., Liu Y.: Computation of rotation minimizing frames. ACM Trans. Graph. 27, 1 (2008), 2:1–2:18.
Kanitsar A., Wegenkittl R., Fleischmann D., Gröller E.: Advanced curved planar reformation: Flattening of vascular structures. In Proceedings of IEEE Visualization (2003), pp. 43–50.